## Slide 1
Midterm Presentation - P4 Accuracy of Approximate Circuits
Fabian Garber, Simon Howind, Kagan Özten, Martin Resetarits, Peter Traunmüller
Notes: Hallo everybody and welcome to our presentation. We are going to present the topic P4 Accuracy of Approximate Circuits

## Slide 2
Introduction
Advantages of approximate computing
Energy-efficient
Less area
Less computing time
2/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 3
Circuit Designs
3/
Notes: Now adding to all the advantages, the question arises How do approximate circuits achieve all of those above mentioned advantages in our design?
As already mentioned, the amount of logic gates is reduced.
For demonstration purposes, we are going to show you two different Full Adder designs. One exact and one approximate.

## Slide 4
Circuit Designs
4/
Conventional Full Adder Circuit Design
Approximate Full Adder Circuit Design as proposed by Priyadharshni et al
Notes: The first design is an exact adder and the second one is an approximate design taken from a paper.
As you can clearly see, the second one is „missing“ some logic gates. The approximate circuit utilizes only 2 exclusive OR's and one NOT gate. The delay is created by three logic gates although the last one is a NOT and much faster than the other gates.
To see what effect it has on the results, we will take a look at the truth tables.

## Slide 5
Truth Table
5/
Notes: In this chart the tick marks show a correct result, and the crosses indicate a wrong bit.
As we can see the sum is always calculated correctly.
However, deviations occur, when calculating the carry out.
Therefore in 6 out of 8 cases, we are calculating the correct carry out.
Error can happen in MSB -> Error is more significant.
This design will be implemented on an open-source processor.
And now we will hear about Error analysis and the future of our project from my colleague Martin.

## Slide 6
Error Analysis
For multi bit inputs, the error is not Hamming distance
Error must be interpreted as number
6/
Notes: In many Boolean functions the error can be interpreted with the help of the Hamming distance.
This was also possible for the one-bit addition presented on the previous slide.
But when we calculate the addition of two multibit numbers the output must also be interpreted as number. So the Hamming distance is no of interest.

## Slide 7
Error Analysis
For multi bit inputs, the error is not Hamming distance
Error must be interpreted as number
7/
EXACT
INXA1
subtract and
absolute
Error
Notes: So the Hamming distance is no of interest.
The error between the exact solution and the approximated solution is the difference. To analyze it we must subtract the two numbers.
As the system grows the complexity grows exponentially with the numbers of inputs.
So a truth table analysis is not recommended anymore.
As solution to this we use a Binary Decision Diagram or short BDD.

## Slide 8
Binary Decision Diagram
8/
Notes: As solution to this we use a Binary Decision Diagram or short BDD. A BDD is an graph to represent the Boolean function.
It consists of nodes, each representing one input Bit, and edges.
An edge represents the value of the input.
The final nodes at the bottom represents the output of the function.
As demonstration we want to present this small example.
We start with X[0]. There are two edges, one for when x[0] = 0 and for x[0] = 1. The edges go to the next Input x[1].
If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.

## Slide 9
Binary Decision Diagram
9/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 10
Current Status
VHDL code for full adder and INXA1 finished
Python code for Binary Decision Diagram for 1 bit analysis
First estimation of power consumption
10/

## Slide 11
Future Plans
Time, Area and Power Analysis with VHDL TOOL
Adding functionality for generic N bit Adders
Implementation in Open Source Processor
Worst Case Error Analysis with BDD
Implementing on Zedboard (Hardware)
11/

## Slide 12
Thank you!
12/