## Slide 1
Midterm Presentation - P4 Accuracy of Approximate Circuits
Fabian Garber, Simon Howind, Kagan Özten, Martin Resetarits, Peter Traunmüller
Notes: Good morning everybody and welcome to our presentation. We are going to present the topic P4 Accuracy of Approximate Circuits

## Slide 2
Introduction
Advantages of approximate computing
Energy-efficient
Less area
Less computing time
1/
Notes: We would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 3
Designed architecture
Presenting our design
*implementing two versions of Full-Adder (one exact and one approximate)
*CIRCUIT DIAGRAMME hinzufügen und Unterschiede erklären mit Hilfe von Tabelle
1/
Notes: Now adding to all the advantages, the question arises How do approximate circuits achieve all of those above mentioned advantages in our design?
As already mentioned, the amount of logic gates is reduced. For demonstration purposed, we are going to show you two different Full Adder design. One exact and one approximate.

## Slide 4
Notes: The first design is an exact adder and the second one is an approximate design taken from a paper.
As you can clearly see, the second one is „missing“ some logic gates.
To see what effect it has, we will take a look at the truth tables.

## Slide 5
Notes: As we can see the sum is always calculated correctly. However deviations occur, when calculating the carry out. In this chart the tik marks show a correct result and the crosses indicate a wrong bit. Therefore in 6 out of 8 cases, we are calculating the correct carry out.
This design will be implemented on an open source processor.

## Slide 6
Progress – Faced Problems - Solutions
VHDL Code
Python Code
6/
Notes: We already wrote the VHDL code for the Full Adders and wrote a Python code that creates a Binary decision tree.
The binary decision tree will be later used to estimate the worst case error.

## Slide 7
Progress – Faced Problems - Solutions
Binary Decision tree BILD
7/
Notes: Erklärung des BDT

## Slide 8
Future Plans
7/
Time, Area and Power Analysis with VHDL TOOL
Implementation in Open Source Processor
Worst Case Error Analysis with BDT
Implementing on Zedboard (Hardware)

## Slide 9
Thank you!
8/