## Slide 1
Midterm Presentation - P4 Accuracy of Approximate Circuits
Fabian Garber, Simon Howind, Kagan Özten, Martin Resetarits, Peter Traunmüller
Notes: Hallo everybody and welcome to our presentation. We are going to present the topic P4 Accuracy of Approximate Circuits

## Slide 2
Introduction
Short Recap
Binary Decision Diagram Progress / Error Analysis
VHDL Progress
Power & Area Analysis
Outlook
2/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 3
Recap: Circuit Designs
3/
Conventional Full Adder Circuit Design
Approximate Full Adder Circuit Design as proposed by Priyadharshni et al
Notes: The first design is an exact adder and the second one is an approximate design taken from a paper.
As you can clearly see, the second one is „missing“ some logic gates. The approximate circuit utilizes only 2 exclusive OR's and one NOT gate. The delay is created by three logic gates although the last one is a NOT and much faster than the other gates.
To see what effect it has on the results, we will take a look at the truth tables.

## Slide 4
Recap: Truth Table
4/
Notes: In this chart the tick marks show a correct result, and the crosses indicate a wrong bit.
As we can see the sum is always calculated correctly.
However, deviations occur, when calculating the carry out.
Therefore in 6 out of 8 cases, we are calculating the correct carry out.
Error can happen in MSB -> Error is more significant.
This design will be implemented on an open-source processor.
And now we will hear about Error analysis and the future of our project from my colleague Martin.

## Slide 5
Recap: Error Analysis
For multi bit inputs, the error is not Hamming distance
Error must be interpreted as number
5/
EXACT
INXA1
subtract and
absolute
Error
Notes: So the Hamming distance is no of interest.
The error between the exact solution and the approximated solution is the difference. To analyze it we must subtract the two numbers.
As the system grows the complexity grows exponentially with the numbers of inputs.
So a truth table analysis is not recommended anymore.
As solution to this we use a Binary Decision Diagram or short BDD.

## Slide 6
Recap: Binary Decision Diagram
6/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 7
What’s New
BDD generation
Worst case error analysis (partly) finished
Area and power analysis of the VHDL design
7/

## Slide 8
Generating BDD for a 2 bit adder
* Generate outputs for exact and approx. adder
*
*
*
*
00 + 00 = approx: 010, exact: 000
00 + 01 = approx: 101, exact: 001
00 + 10 = approx: 100, exact: 010
00 + 11 = approx: 011, exact: 011
01 + 00 = approx: 101, exact: 001
01 + 01 = approx: 010, exact: 010
01 + 10 = approx: 011, exact: 011
...
8/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 9
Generating BDD for a 2 bit adder
* Generate outputs for exact and approx. adder
* Calculate error
*
*
*
00 + 00 = approx: 010, exact: 000, error: 1
00 + 01 = approx: 101, exact: 001, error: 1
00 + 10 = approx: 100, exact: 010, error: 1
00 + 11 = approx: 011, exact: 011, error: 0
01 + 00 = approx: 101, exact: 001, error: 1
01 + 01 = approx: 010, exact: 010, error: 0
01 + 10 = approx: 011, exact: 011, error: 0
...
9/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 10
Generating BDD for a 2 bit adder
* Generate outputs for exact and approx. adder
* Calculate error
* Extract truth tables
*
*
00 + 00 = approx: 010, exact: 000, error: 1
00 + 01 = approx: 101, exact: 001, error: 1
00 + 10 = approx: 100, exact: 010, error: 1
00 + 11 = approx: 011, exact: 011, error: 0
01 + 00 = approx: 101, exact: 001, error: 1
01 + 01 = approx: 010, exact: 010, error: 0
01 + 10 = approx: 011, exact: 011, error: 0
...
10/
bit 0
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 11
Generating BDD for a 2 bit adder
* Generate outputs for exact and approx. adder
* Calculate error
* Extract truth tables
* Draw for bits
*
00 + 00 = approx: 010, exact: 000, error: 1
00 + 01 = approx: 101, exact: 001, error: 1
00 + 10 = approx: 100, exact: 010, error: 1
00 + 11 = approx: 011, exact: 011, error: 0
01 + 00 = approx: 101, exact: 001, error: 1
01 + 01 = approx: 010, exact: 010, error: 0
01 + 10 = approx: 011, exact: 011, error: 0
...
11/
bit 0
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 12
Generating BDD for a 2 bit adder
* Generate outputs for exact and approx. adder
* Calculate error
* Extract truth tables
* Draw BDD for bits
* Draw BDD for error
00 + 00 = approx: 010, exact: 000, error: 1
00 + 01 = approx: 101, exact: 001, error: 1
00 + 10 = approx: 100, exact: 010, error: 1
00 + 11 = approx: 011, exact: 011, error: 0
01 + 00 = approx: 101, exact: 001, error: 1
01 + 01 = approx: 010, exact: 010, error: 0
01 + 10 = approx: 011, exact: 011, error: 0
...
12/
error
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 13
BDD: Complexity
Example:
* 8 bit full adder
* 2^(8*2) = 65536 input combinations
* BDDs for output bit „1“
 Approximate: 31 nodes
Exact: 49 nodes 
13/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 14
BDD: Complexity
Example:
* 8 bit full adder
* 2^(8*2) = 65536 input combinations
* BDDs for output bit „1“
 Approximate: 31 nodes
Exact: 49 nodes 
14/
* 64 bit adder ?
* 2^(64*2) = 3.4E38 input combinations
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 15
BDD: Error
15/
* Error BDD for 8 bit adders
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 16
BDD: Error Analysis
16/
Adapted from: Z. Vasicek: Formal Methods for Exact Analysis of Approximate Circuits
00 + 00 = approx: 010, exact: 000, error out: 2
00 + 01 = approx: 101, exact: 001, error out: 4
00 + 10 = approx: 100, exact: 010, error out: 2
00 + 11 = approx: 011, exact: 011, error out: 0
01 + 00 = approx: 101, exact: 001, error out: 4
01 + 01 = approx: 010, exact: 010, error out: 0
01 + 10 = approx: 011, exact: 011, error out: 0
...
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 17
BDD: Error Analysis
17/
00
01
10
11
00 01 10 11
A in
B in
0
2
4
Error distance
2 bit adder
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 18
BDD: Error Analysis
18/
8 bit adder
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 19
VHDL in Detail
What has been done so far:
1-,4-,8- and 16-bit full adders in exact and approximate form is completed
Schematics regarding these designs are realised
Area and power analysis of the VHDL design are partially done
19/

## Slide 20
VHDL: Schematics
Exact vs. Approximate: reduced basic logic gate number
1-Bit Full Adder:
1-Bit Approximate Full Adder (INXA1):
20/
Notes: What we have here is an elaborated design of our VHDL code automaticly generated by Vivado.
As you can see; 1 Bit exact full adder has 2 XOR, 2 AND and 1 OR gate. On the other hand in approximate design (INXA1) we have 2 XOR and 1 NOT gate intact.
Bear in mind that XOR gate is consist of 1 AND, 1 NAND and 1 OR gate. Which is equivalent to 4 basic gates in total.

## Slide 21
Area Analysis
[Kagan: bitte einfügen]
Exact Adder
Approximate Adder
21/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 22
Power Analysis
Exact Adder
Approximate Adder
22/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 23
Future Plans
Adding functionality for generic N bit Adders
Final Worst Case Error Analysis with BDD
Several Graphical Error Visualisations
Implementing on Zedboard (Hardware)
23/

## Slide 24
Thank you!
24/