## Slide 1
Final Presentation - P4 Accuracy of Approximate Circuits
Fabian Garber, Simon Howind, Kagan Özten, Martin Resetarits, Peter Traunmüller
Notes: Hallo everybody and welcome to our presentation. We are going to present the topic P4 Accuracy of Approximate Circuits

## Slide 2
Table of Content
Goals
Methods
Results
    Error Analysis
    Timing Analysis
    Power Consumption & Area
Conclusion
1/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 3
Goals
Comparison of exact and approximate Full-Adder
Power Consumption & Area evaluation
Systematic error analysis
VHDL implementation
1/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 4
Goals
Comparison of exact and approximate Full-Adder
Power Consumption & Area evaluation
Systematic error analysis
VHDL implementation
1/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 5
Methods
1/

## Slide 6
Methods – Design Comparison
1/
Conventional Full Adder Circuit Design
Approximate Full Adder Circuit Design as proposed by Priyadharshni et al
Notes: The first design is an exact adder and the second one is an approximate design taken from a paper.
As you can clearly see, the second one is „missing“ some logic gates. The approximate circuit utilizes only 2 exclusive OR's and one NOT gate. The delay is created by three logic gates although the last one is a NOT and much faster than the other gates.
To see what effect it has on the results, we will take a look at the truth tables.

## Slide 7
Methods – Result Comparison
1/
Notes: In this chart the tick marks show a correct result, and the crosses indicate a wrong bit.
As we can see the sum is always calculated correctly.
However, deviations occur, when calculating the carry out.
Therefore in 6 out of 8 cases, we are calculating the correct carry out.
Error can happen in MSB -> Error is more significant.
This design will be implemented on an open-source processor.
And now we will hear about Error analysis and the future of our project from my colleague Martin.

## Slide 8
Methods - Error Analysis
For multi bit inputs, the error is not Hamming distance
Error must be interpreted as number
8/
EXACT
INXA1
subtract and
absolute
Error
Notes: So the Hamming distance is no of interest.
The error between the exact solution and the approximated solution is the difference. To analyze it we must subtract the two numbers.
As the system grows the complexity grows exponentially with the numbers of inputs.
So a truth table analysis is not recommended anymore.
As solution to this we use a Binary Decision Diagram or short BDD.

## Slide 9
Methods - Binary Decision Diagram
9/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 10
Methods – BDD Complexity
Example:
8 bit full adder
2^(8*2) = 65536 input combinations
BDDs for output bit „1“
<= Approximate: 31 nodes
Exact: 49 nodes =>
10/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 11
Methods – BDD Complexity
Example:
8 bit full adder
2^(8*2) = 65536 input combinations
BDDs for output bit „1“
<= Approximate: 31 nodes
Exact: 49 nodes =>
11/
64 bit adder ?
2^(64*2) = 3.4E38 input combinations
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 12
Methods - VHDL Implementation
Vivado used for:
                  Power consumption analysis
                  Area analysis
                  Timing analysis
12/
Notes: What we have here is an elaborated design of our VHDL code automatically generated by Vivado.
As you can see; 1 Bit exact full adder has 2 XOR, 2 AND and 1 OR gate. On the other hand in approximate design (INXA1) we have 2 XOR and 1 NOT gate intact.
Bear in mind that XOR gate is consist of 1 AND, 1 NAND and 1 OR gate. Which is equivalent to 4 basic gates in total.

## Slide 13
Methods - VHDL Implementation
Exact vs. Approximate: reduced basic logic gate number
1-Bit Full Adder:
1-Bit Approximate Full Adder (INXA1):
13/
Notes: What we have here is an elaborated design of our VHDL code automatically generated by Vivado.
As you can see; 1 Bit exact full adder has 2 XOR, 2 AND and 1 OR gate. On the other hand in approximate design (INXA1) we have 2 XOR and 1 NOT gate intact.
Bear in mind that XOR gate is consist of 1 AND, 1 NAND and 1 OR gate. Which is equivalent to 4 basic gates in total.

## Slide 14
Results
13/

## Slide 15
Results - BDD: Error Analysis
15/
Adapted from: Z. Vasicek: Formal Methods for Exact Analysis of Approximate Circuits
00 + 00 = approx: 010, exact: 000, error out: 2
00 + 01 = approx: 101, exact: 001, error out: 4
00 + 10 = approx: 100, exact: 010, error out: 2
00 + 11 = approx: 011, exact: 011, error out: 0
01 + 00 = approx: 101, exact: 001, error out: 4
01 + 01 = approx: 010, exact: 010, error out: 0
01 + 10 = approx: 011, exact: 011, error out: 0
...
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 16
Results - BDD: Error
16/
Error BDD for 8 bit adders
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 17
Results – Visual Error Analysis
17/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 18
Results – Timing Analysis
18/
Notes: If both x[0] and x[1] are 0 then the solution is 0, so the edge goes directly to the 0.
The other path to reach the 0 is with 0, 1, 0.
This reduction of possible paths lead to a much smaller representation then a truth table.
It is possible to compute and analyze BDD automatically. This includes checking for satisfiability, tautologies, and value inserting.
The complexity only grows either linear or quadratic with the number of inputs for these operations. (Exact numbers in “An Introduction to BDDs” by Henrik Reif Andersen).
With this technique, the analyzes can be done in an efficient way.

## Slide 19
Results - Power Consumption
19/
16 BIT
4 BIT
EXACT
APPROXIMATE
Notes: In 16 Bit design, the difference in power consumption reaches to almost 50% (49.33%).

## Slide 20
Results - Area Analysis
Used metric for area: Gate Count in adders
20/
TYPE | XOR | OR | AND | NOT | Basic Gates in Total
1 Bit Exact | 2 | 1 | 2 | X | 11
4 Bit Exact | 8 | 4 | 8 | X | 44
8 Bit Exact | 16 | 8 | 16 | X | 88
16 Bit Exact | 32 | 16 | 32 | X | 176
1 Bit Appro. | 2 | X | X | 1 | 9 (-3)
4 Bit Appro. | 8 | X | X | 4 | 36 (-8)
8 Bit Appro. | 16 | X | X | 8 | 72 (-16)
16 Bit Appro. | 32 | X | X | 16 | 144 (-32)
XOR = 2 AND + 1 OR + 1 NOT = 4 Basic Gates
= ~18.2% less
Notes: This is still in early stage. But basically what we initially thought is that gate count number is a good indicator for how much space we can actually save.
Before the demo presentation i‘m thinking to expand these area and power analysis sections with more detail.
And for that we can use for example; Synopsys Design compiler. With these Design Compiler we will have more precise number in analysis.

## Slide 21
Conclusion
20/

## Slide 22
Achieved Goals
Comparison of exact and approximate Full-Adder
Power Consumption & Area evaluation
Systematic error analysis
VHDL implementation
20/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 23
Outlook
Implementation on FPGA board
Using an actual design
20/
Notes: I would like to start with a small introduction about approximate computing and its advantages compared to conventional circuits.
According to multiple papers, it has shown to be one of the most promising energy-efficient paradigms and has therefore reached a lot of research attention.
Another advantage of the approximate circuits is that the hardware uses less space due to the reduced number of logic gates.
For the same reason it has a reduced delay time and produces faster results.

## Slide 24
20/
Thank you!